Staying Home Corporation

1503 Vine Street

P.O. Box 37

Harrisonville, MO  64701

816.380.2427

www.stayinghome.com

Legacy® Stairlift Specifications

Manufactured by Staying Home Corporation

PART 1		GENERAL

1.1 	PRODUCT SUMMARY:

A.   	Legacy Classic – rigid arm stair-lift designed to meet A18.1 Sections 4 & 7

B.   	Legacy Elegance – folding arm stair-lift designed to meet A18.1 Sections 4 & 7

C.	Legacy Outdoor – folding arm stair-lift designed to meet A18.1, Sections 4 & 7

.

1.2 	REFERENCES:

Legacy Stairlifts are designed, manufactured and to be installed in accordance with the following standards:

A.   	American Welding Society (AWS)

B.   	American Society for Testing Materials (ASTM)

C.   	ANSI  A117.1

D.   	National Electrical Code (NEC)

E.  	ETL Listed

1.3 	DESIGN REQUIREMENTS:

A. 	Constant pressure controls

B.      	Motor brake

C.	Rack and pinion drive

D.	24 VDC gear motor

E.	2 arms on folding seat

F.	Seat belt

G.	Standard limit switches at each end

H.	Final limit at top with mechanical stops at each end

I.	Directional footrest sensors

J.	Seat swivel switch

K.	3 position seat swivel mechanism at top landing

L.	Aluminum extrusion track

M.	Adjustable charging points at each end of track

N.	Speed of between 16 – 24 feet per minute

O.	Capacity of 350 lbs.

1.4     PERFORMANCE REQUIREMENTS:

A.	Cooperate with local regulatory agency or authority and provide data as requested by authority having jurisdiction.

B.	Provide decal on unit attesting to ETL / ANSI A18.1 certification.

1.5	SUBMITTALS

A.	Product Data:  Manufacturer's data sheets on each product to be used, product metals & finishes available upon request.

B.	Preparation instructions and recommendations

C.	Manufacturer’s installation instruction methods.

D.	Shop Drawings: Include plan views, sections, door details, and anchor detail.

E.	Warranty Documentation as detailed in Owner’s Manual

1.6	QUALITY ASSURANCE:

A.	Manufacturer Qualifications: Company specializing in manufacturing stairlifts with a minimum of twenty years’ experience in manufacturing and fabrication processes. A quality assurance program utilizing an independent third party to test each system design to industry standards.

B.	Prefabricated Components: Comply with manufacturer's published literature for products meeting indicated design loads in accordance with state and local requirements as applicable.

C.	DELIVERY, STORAGE, AND HANDLINGS: Store products in manufacturer's unopened packaging until ready for installation.

D.	Protect all components and accessories from corrosion, deformation, damage and deterioration when stored at job site. Keep materials free from dirt and foreign matter.

1.7	PROJECT CONDITIONS:

Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results. Do not install products under environmental conditions outside manufacturer's absolute limits.

1.8 	WARRANTY:

A.	Manufacturer's Warranties:  Provide manufacturer's limited warranty on products to be free of defects in materials and workmanship from date of shipment.

B.	Provide copies of the third party manufacturer's warrantees on all optional accessory items provided.

END OF SECTION